## Slide 1: Ecological Integrity Assessment of Maine Wetlands
Andy Cutko
Maine Natural Areas Program
March 2016

## Slide 2: Topics to Be Covered
Background on Ecological Integrity Assessment
Development of EIA for use in Maine
A Tale of Two Swamps - Real Life Examples!
Take Home Messages
Notes: True collaborative project - Don FL and Bill Nichols, funded by EPA

## Slide 3: What is Ecological Integrity Assessment?
A set of indicators of ecosystem structure, function, and composition
Emphasis on range of natural variation – and what’s outside it!
Ensure links with management/restoration needs
National protocols, currently being used in NH, NY, NJ, CO, WA, MI, NM
Notes: In the NatureServe approach, EI is assessed through a set of …
Bullet 3 – idea is to use in both wetland protection and restoration
Three Pillars – size, condition, LC
Currently being used by New Hampshire, New Jersey, NY, Colorado, Washington, New Mexico, others

## Slide 4: Wetland Assessments: Functions, Values, and Integrity
Conservation Values
Condition / Integrity
Ecosystem Services
Functional
Measures
Ecological Integrity
Measures
Conservation
Status/
Irreplaceability
Notes: There are a number of approaches and perspectives and wetland assessment and classification. Traditionally, heritage programs focus on VALUES – (left side) rarity, size, uniqueness, irreplaceability – while some regulatory approaches focus more on FUNCTIONS – floodflow alteration, water quality enhancement. EIA combines elements of both.

## Slide 5: Topics to Be Covered
Background on EIA
Development of EIA for use in Maine
A Tale of Two Forests - Real Life Examples!
Take Home Messages
Notes: About three years ago our program received a grant from EPA… to apply EIA methods to Maine.
One of the challenges is to adapt a national model to ME, when the national model is meant to apply to wetlands ranging from Prairie Potholes to North Carolina Pocosins.

## Slide 6: EIA in Maine: Accomplishments to Date
Reviewed protocols and manuals from NatureServe, NH, and others
Field tested EIA methods (and FQA) on 70+ floodplain forests and red maple swamps
Developed relational database to store, process data
Adapting protocols and manual for Maine use

## Slide 7: Topics to Be Covered
Background on EIA
Development of EIA for use in Maine
A Tale of Two Forests - Real Life Examples!
Take Home Messages

## Slide 8
Messalonskee Stream
Waterville Maine
Hardwood River Terrace Forest
Size: 11 ac
Size Rank = C
Notes: Small site in central Maine – one of the few areas in Maine that would truly be called urban. Some historic loss at southwestern side.

## Slide 9
Size Ranks for Maine Natural Communities (Acres)
Notes: Sizes are generally in line with NS guidelines on patch size – small, large, matrix – the way natural communities lie on the landscape.

## Slide 10
Condition
Vegetation
Composition
Regeneration
Invasive Cover
Structure
Hydrology
Water source
Hydroperiod
Connectivity
Soils
Disturbance
Physical patch diversity

## Slide 11
Notes: We’ve taken language on metrics and thresholds from NH.

## Slide 12
Condition
Hydrology
Soil
Vegetation
Weighted coefficent of conservatism = 1.29
Notes: 100 year old dam immediately upstream has altered hydrology; one of lowest WCoC values encountered in floodplain forests.

## Slide 13: Stressors Checklist
Notes: Can be used in a quantiative or scoring fashion as ancillary data, or just as a list of things to consider in evaluating the site and landscape context.

## Slide 14
Condition = D (2.6)
Vegetation 2.0
Composition D (1)
Regeneration C (3)
Invasive Species D (1)
Structure C (3)
Hydrology 2.0
Water source D (1)
Hydroperiod D (1)
Connectivity B (4)
Soils 3.0
Disturbance C (3)
Physical patch diversity C (3)
Notes: Connectivity – refers to immediate connectivity between FP forest and water – some areas of rip-rap but largely connected.

## Slide 15
Landscape Context
50
250
500
Notes: Buffer –
Surrounding land use
Landscape Connectivity
Created a GIS tool USING WHAT COVER???

## Slide 16: Land Use Index
Using Land cover data in a GIS:
Each cover type is assigned a coefficient value
Current Land Use | Coefficient
Paved roads / parking lots / domestic or commercially developed buildings / mining (gravel pit, quarry, open pit, strip mining) | 0
Unpaved roads (e.g., driveway, tractor trail) / abandoned mines | 0.1
Agriculture (tilled crop production) / intensively developed vegetation (golf courses, lawns, etc.) | 0.2
Vegetation conversion (chaining, cabling, rotochopping, clearcut) | 0.3
Heavy grazing on rangeland or pastures | 0.3
Heavy logging or tree removal with 50-75% of trees >30 cm dbh removed | 0.4
Intense recreation (ATV use / camping / sport fields / popular fishing spot, etc.) / military training areas (armor, mechanized) | 0.4
Agriculture - permanent crop (vineyards, orchards, nurseries, berry production, introduced hay field and pastures, etc.) | 0.4
Commercial tree plantations / Christmas tree farms | 0.5
Dam sites and flood disturbed shorelines around water storage reservoirs | 0.5
Recent old fields and other disturbed fallow lands dominated by ruderal and exotic species | 0.5
Moderate grazing on rangeland | 0.6
Moderate recreation (high-use trail) | 0.7
Mature old fields and other fallow lands with natural composition | 0.7
Selective logging or tree removal with <50% of trees >30 cm dbh removed | 0.8
Light grazing / light recreation (low-use trail) / haying of native grassland | 0.9
Natural area / land managed for native vegetation | 1
* Modified from Hauer et al. 2002
Notes: Paved roads – O to intact forest 1.0

## Slide 17
Land Use Index Scoring Table
  Overall land use index is then assigned a metric rating
  Weight of index values in each of the three concentric zones toward overall score…
  Buffer (0-50): 60%
  Surrounding land use (50-250): 25%
  Landscape connectivity (250-500): 15%
Metric Rating (National ) |  |  | 
Excellent (A) | Good (B) | Fair (C) | Poor (D)
0.95 - 1.0 | 0.80 - 0.94 | 0.4 - 0.79 | < 0.4

## Slide 18
Landscape Context = 0.52 (C)
Notes: Justin – which land cover layer did we use??

## Slide 19
Landscape Context: Manual Override
LC =0.65 (C)

## Slide 20: Ecological Integrity Assessment
Overall wetland rank = D (2.13)
LC
Stressor
Checklist
LC Rank Specs
Size Rank Specs
Size Metrics
Size = C
Condition Metrics
Condition = C
LC Metrics
LC = B
Condition Rank Specs
Condition Rank = D
LC Rank = D
Condition
Stressor
Checklist
Size Rank = C
EIA Level Rapid Recon Form
Plot data
Post-Field
General
Form
Field
Landscape
Context
GIS
Calculation
Metric1
Metric1 : Relative
Metric2 Absolute
Vegetation
Metric1
Metric2
|
Metric7
Soil/Substrate
Metric1
Metric2
Metric3
Hydrology
Metric1
Metric2
Metric3
Pre-Field

## Slide 21
A > 4.5
B = 3.5 – 4.5
C = 2.5 - 3.5
D < 2.5
Letter Grades indicate ‘Excellent, Good’ Fair, Poor’

## Slide 22: West Branch of the Pleasant River Silver Maple Floodplain Forests T6 R9 NWP
Size = 502 Acres (A)

## Slide 23
Condition
Vegetation
Hydrology
Soils

## Slide 24
WC = 4.35 (FQI)
Wood nettle
Ostrich fern

## Slide 25
Condition = A (4.73)
Vegetation 5.0
Composition A (5)
Regeneration A (5)
Invasive Species A (5)
Structure A (5)
Hydrology 5.0
Water source A (5)
Hydroperiod A (5)
Connectivity A (5)
Soils 4.5
Disturbance B (4)
Physical patch diversity A (5)
Notes: \

## Slide 26
Landscape Context = 0.92 (B)

## Slide 27: Ecological Integrity Assessment
Overall wetland system rank = A (4.73)
LC
Stressor
Checklist
LC Rank Specs
Size Rank Specs
Size Metrics
Size = A
Condition Metrics
Condition = A
LC Metrics
LC = B
Condition Rank Specs
Condition Rank = A
LC Rank = B
Condition
Stressor
Checklist
Size Rank = A
EIA Level Rapid Recon Form
Plot data
Post-Field
General
Form
Field
LC Index
GIS
Calculation
Metric1
Metric1
Metric2
Vegetation
Metric1
Metric2
|
Metric4
Soil/Substrate
Metric1
Metric2
Metric3
Hydrology
Metric1
Metric2
Metric3
Pre-Field

## Slide 28: EIA: Take Home Messages
EIA provides a more consistent, repeatable method for evaluating wetland condition and conservation value
Work by NatureServe, NH Heritage and others has provided a foundation for use of EIA across the region
Further work is needed to develop a reference set of EIA scores for wetlands to help calibrate scores (NWCA?)

## Slide 29
Questions?
andrew.cutko@maine.gov