## Slide 1: Update on the New England Wetland Functional Assessment
Paul Minkin
U.S. Army Corps of Engineers
Erica Sachs Lambert
U.S. Environmental Protection Agency
Maine Association of Wetland Scientists
31 March 2016

## Slide 2: Basic methodology criteria
Regionally applicable
  Datasets must be regionally consistent
FUNCTIONAL assessment
  Not condition assessment (biota exception)
  Not assessing services (= “values”)
Independent score for each function
  NO TOTAL FUNCTIONAL SCORE
Practicable (time and resources)
Objective (repeatable)

## Slide 3: Structure of Method
Same model for all hydrogeomorphic subclasses
  Functional score will be 0 when not applicable
Three categories of functions:
  1) Water quality maintenance
  2) Hydrologic integrity
  3) Biota support
Extra Focus Triggers
  Red flags for extra scrutiny during review
  Examples: Endangered species, impaired waters, upstream pollutant source
Stressors – data collected but not used in models

## Slide 4: Functions
WATER QUALITY MAINTENANCE
Particulate retention
Removing heavy metals and toxic organics
Nutrient transformation – Phosphorus
Nutrient transformation – Nitrogen
Carbon sequestration
BIOTA SUPPORT
Production export
Plant community integrity
Wildlife habitat integrity
HYDROLOGIC INTEGRITY
Groundwater recharge
Streamflow maintenance
Surface water detention
Storm surge detention
Bank and shoreline stabilization

## Slide 5: Variables and scoring
Data (field or desktop) collected used to determine score for variables
Scoring is specific to each model
Some variables are used in multiple models
  Example: Landscape Position is used in four different models
          Particulate Retention
          Groundwater Recharge
          Surface Water Detention
          Groundwater Discharge (variable model)
Scoring can be a range or binary (presence/absence)
Classification data is converted to a score by ranking values
Lowest score maybe 0 or 1 depending on variable and model

## Slide 6: Functional Capacity Models
Models determine functional capacity score (not potential function)
All Models are scored from 0-10
Model score 0 = FUNCTION IS NOT APPLICABLE
  Example: Stream Flow Maintenance does not occur if no stream
Models = Variables combined in equations
Some variables are scored so that Function = 0
Some variables are scored to only add/subtract 1-2 points to total model score
  Example: High evapotranspiration lowers score for Stream Flow Maintenance by 1-2 points

## Slide 7: End result
Score for each individual function
  Possibly scores for each functional category
  NO TOTAL FUNCTIONAL SCORE
Determines functional capacity
Scores do not portray false level of precision
0 | Function does not occur (N/A)
1 to 3 | Low functioning
4 to 6 | Moderately functioning
7 to 10 | High functioning

## Slide 8: Development process to date
Developed basic criteria
Developed list of functions to assess
Reviewed many existing wetland assessments
  including Highway Methodology Supplement, several state assessment methods, several HGM models
Incorporated features from other methods
Developed draft models
Field testing data collection and analysis
CURRENTLY using field testing results to revise and validate models

## Slide 9: Field Testing 2015
ME15-01a Reid State Park salt marsh (lower) Georgetown ME
ME15-01b Reid State Park salt marsh (upper) Georgetown ME
ME15-02 Reid State Park (Ice Pond) Georgetown ME
20 additional sites
Total 23 sites across all six New England states

## Slide 10: Example: Particulate Retention
Model
Position = landscape position, HGM class
Outlet Type = system discharge
Velocity Reduction = sub-variable based on vegetation and microfeatures

## Slide 11: Example – NH15-03 (The Greens)
49 acres scrub-shrub bog surrounded by forest
HGM Class = Depressional
Multiple Surface Outlets
  Least Restrictive Outlet = Stream Channel (<25% of site width)`

## Slide 12: NH15-03 Vegetation Data
3 Veg Plots: Shrub (46%), Herbaceous (52%), Forest/Herbaceous (2%)
Overall Veg Cover: 98%, 90%, 90% Weighted Average = 94%
Shrub Cover: 90%, 20%, 20% Weighted Average = 52%
Persistent Herb Cover: 10%, 90%, 10% Weighted Average = 52%
Non-Persistent Herb Cover: 0%, 10%, 50% Weighted Average = 6%
Tree Stem Count (per 100m2): 1, 0, 4 Weighted Average = 1 tree
  Score by Class: Trees per 100m2 1- 4 trees = 5pts
Microfeatures (boulders, hummocks, coarse woody material) per 100 ft:
  Score by Class: Features per 100ft 3 features
  1- 4 features = 5pts

## Slide 13: Begin by calculating Velocity Reduction sub-variable
Variables
Used:
Overall vegetative cover = 94
Persistent herbaceous cover = 52
Non-persistent herbaceous cover = 6
Shrub cover = 52
Tree stem density = 5
Microfeatures = 5
VELOCITY REDUCTION SCORE = 9

## Slide 14: Now calculate Particulate Retention:
Position = Depressional = 10
Outlet Type (least restrictive outlet) =
  Stream Channel (<25% of site width) = 8
Velocity Reduction = 9
PARTICULATE RETENTION
SCORE = 9

## Slide 15: Example – NH15-02 (Bedell Bridge Drainage Way)
0.23 acre herbaceous floodplain/drainageway
HGM Class = Riverine
Single Surface Outlet
Least Restrictive Outlet = Stream Channel,
> 75% of site width

## Slide 16: Begin by calculating Velocity Reduction sub-variable
Variables
Used:
Overall vegetative cover = 80
Persistent herbaceous cover = 2
Non-persistent herbaceous cover = 50
Shrub cover = 10
Tree stem density (6 stems) = 10
Microfeatures (avg 3 features) = 5
VELOCITY REDUCTION SCORE = 4

## Slide 17: Now calculate Particulate Retention:
Position = Riverine = 7
Outlet Type (least restrictive outlet) =
  Stream Channel (>75% of site width) = 0
Velocity Reduction = 4
PARTICULATE RETENTION
SCORE = 4

## Slide 18: Particulate Retention Scores
NH15-01 | 6 | RI15-01 | 3
NH15-02 | 4 | RI15-02 | 3
NH15-03 | 9 | RI15-02a | 3
NH15-04 | 4 | RI15-02b | 2
VT15-01 | 10 | MA15-01 | 10
VT15-02 | 5 | MA15-02 | 6
VT15-03 | 9 | MA15-02a | 6
ME15-01 | 6 | MA15-02b | 6
ME15-01a | 5 | CT15-01 | 4
ME15-01b | 7 | CT15-02 | 9
ME15-02 | 3 | CT15-03 | 4
 |  | CT15-04 | 4

## Slide 19: Next Steps
Continue running field testing data through remaining models
Revise models as necessary
Complete guidebook for method
Public notice for draft method and field testing
Finalize method

## Slide 20: Questions?
For more information contact:
Paul.Minkin@usace.army.mil
Or
Sachs.Erica@epa.gov